## Slide 1: Optimization of Swimming Fin
Jiujiu (Joey) Lou
August 2018
University of Tokyo

## Slide 2: Steps Taken
Understand and implement Genetic Algorithm
Understand physical simulation (FEM)
Interpret results from simulation
Perform optimization

## Slide 3: Genetic Algorithm, Knapsack
A T
G C

## Slide 4: Fitness evaluation Crossover between parents Mutation Move from generation to generation Key Features

## Slide 5: Variables Implementations
Crossover probability
Mutation probability
Population size
Generation number
Binary representation of Knapsack problem
Single point crossover
Point-wise mutation
Roulette selection

## Slide 6
Single-point crossover
Point-wise Mutation

## Slide 7: Roulette Selection
Finding a random fraction between 0 and 1, then the corresponding individual on cumulative density function will be selected as one of the parent.
Here, number 0.51 is generated, which corresponds to individual 12 on the curve.

## Slide 8: Variables Results
Higher mutation probability
Higher crossover rate
Larger population size
More generations
Longer to converge, but less likely to stuck in local optimum
More searching between high fitness individuals
Larger search space
More time to converge

## Slide 9: Real Coded Genetic Algorithm
Minimize Unimodal function: F=(X₁)²+(X₂)²+(X₃)².

## Slide 10: Outline
Selection method:
  Roulette
  Tournament
Crossover method:
  Laplace
  BLX-alpha
  Arithmetic
Mutation method:
  Power
  Uniform
3 input variables and many different methods to try

## Slide 11: Evaluation
All combinations of methods aforementioned are tested out and ran till generation 100.
Best runs correspond to ‘100/200’, which uses:
BLX-alpha/ Laplace crossover
Uniform mutation
Tournament selection

## Slide 12: BLX-alpha
Given two parents, P₁, P₂ and determine offspring O₁.
I = | P₁- P₂ |
a = max(P₁, P₂) + I*𝜶
b = min(P₁, P₂) - I*𝜶
O₁ = random (a, b)
Crossover method

## Slide 13: Laplace
Given two parents, P₁, P₂ and determine offsprings O₁, O₂.
𝜶 = random(0,1)
𝜷 = a ± b*log(𝜶)
O₁ = P₁ + 𝜷*| P₁ - P₂ |
O₂ = P₂ + 𝜷*| P₁ - P₂ |
Crossover method

## Slide 14: Uniform
r = random(0,1)
Xᵢ = Xᵢ ± delta*r
Equal chance for both signs, delta shrinks as generation moves on and eventually reaches zero.
Mutation method

## Slide 15: Tournament
A number of individuals will be selected from whole population to participate in a “tournament”.
The fittest individual from the group will be selected as the parent.
The larger the tournament size, the more discriminative the selection process will be.
Selection method

## Slide 16: 1D Rod Extension FEM
Referenced chapter 3 in Finite Element Method book.

## Slide 17: Problem setup
E = 1000
L = 10
bₓ = 10 ( 0 < X < 5 )
tₓ = 25
1-D rod extension

## Slide 18: Results
Even with first order shape functions, we can achieve reasonable results.

## Slide 19: Interpret FSI Data
Evaluate power (energy) and velocity.

## Slide 20: Sinusoidal input
Dirichlet conditions are imposed onto first node of beam, where y position and angle 𝜃 are fixed.
y = 0
𝜃 = α*sin(2𝜋*𝑓*𝛥𝑡*n), where n is iteration number, 𝛥𝑡 is time step.

## Slide 21: Torque vs theta
Circular patterns can be seen.
The number of circles corresponds to number of input cycles (sine wave).
At startup, the pattern is not stable.

## Slide 22: Power input over time
Power at iteration i:
Pᵢ = (𝜽ᵢ - 𝜽ᵢ₋₁)*(𝜏ᵢ + 𝜏ᵢ₋₁)/(2*𝛥𝑡)
Average power:
Pavg = 𝛴 P / (N-1) , where N is max iteration
Negative power is achieved when torque acts in the opposite direction of movement.

## Slide 23: Velocity over time
Velocity at iteration i:
Vᵢ = (𝑥ᵢ - 𝑥ᵢ₋₁)/𝛥𝑡
Average velocity:
Vavg = 𝛴 V / (N-1)

## Slide 24: Optimize Fin
Apply RCGA to achieve balance between power and velocity.

## Slide 25: Input
Input wave for angle 𝜃:
𝜃 = α*sin(2𝜋*𝑓*𝛥𝑡*n)
We control two variables:
α = Amplitude, 𝑓 = frequency

## Slide 26: RCGA
Evaluation function for fitness:
F = V^(2.75)/P
Range for input variables:
α ∈ [0.1, 1], 𝑓 ∈ [2, 10]
Population size: 30.
Generation number: 100.

## Slide 27: Sample Run
Each point corresponds to a FSI simulation.
Blue line represents the path taken by highest fitness score in each generation.
High fitness trials cluster around light yellow belt section.

## Slide 28: Sample Run
Best individual in final generation:
A=0.787778,
F=5.877350,
FIT=1633.676761.
Fitness score are very close to each other.

## Slide 29: Convergence
Two methods differ only in crossover methods (BLX-alpha and Laplace).
Both converged to:
A=0.787251, F=5.869870, FIT=1633.506547
A=0.787778, F=5.877350, FIT=1633.676761

## Slide 30: Generation 1

## Slide 31: Generation 20 - Solution becomes homogeneous.

## Slide 32: Generation 100 - Global optimum reached.

## Slide 33: Further Developments
Optimize existing RCGA.
Expand input space using Fourier series.

## Slide 34: Avoid Local Optimums
Problems:
Multiple local optimums exist.
Reached homogeneity too quickly.
Existence of errors.
Possible Solutions:
Tune GA parameters for faster and better convergence.
Try other methods.
Reformulate the evaluation function.
Enlarge the simulation space.

## Slide 35: Use Different Inputs
Input in Fourier series:
𝜃 = α₁*sin(2𝜋*𝑓*𝛥𝑡*n)+α₂*sin(2𝜋*2𝑓*𝛥𝑡*n)
Result:
A1=0.560227, A2=0.193823,
F=5.111914, FIT=1595.007598.

## Slide 36: Solution with input from previous slide:

## Slide 37: End of Research Presentation
Questions?